## Slide 1: Pore-resolved simulations of ammonia combustion in porous inert media
Rishabh Puria*, Thorsten Zirwesb, Oliver T. Steina
Deutscher Flammentag, Paderborn University
15-17th September 2025
a Karlsruhe Institute of Technology, Engler-Bunte-Institute, Thermo-Fluid Systems
b University of Stuttgart, Institute of Reactive Flows
N
H
H
H

## Slide 2: Content
Ammonia as a fuel
Porous media combustion
Numerical modelling of ammonia combustion
Flame structure
Ammonia dehydrogenation
Results
Conclusions and outlook

## Slide 3: Ammonia as a fuel
Ammonia end-use1
1. R.F. Service, Ammonia—a renewable fuel made from sun, air, and water could power the globe without carbon, Science, 2018.
Carbon free fuel
H2 carrier
Can be transported using the existing infrastructure
Why ammonia?

## Slide 4: Ammonia as a fuel
High toxicity at trace levels
High NOx emissions
Poor flame stability
Challenges
1D premixed free-flame simulations
(Reproduced from Kobayashi et al.4)
Experimental measurements
Krejci et al., https://doi.org/10.1115/1.4007737
Vagelopoulos et al., https://doi.org/10.1016/S0082-0784(98)80441-4
Mei et al., https://doi.org/10.1016/j.combustflame.2019.08.033
Kobayashi et al., https://doi.org/10.1016/j.proci.2018.09.029

## Slide 5: Porous media combustion
Increased effective burning velocity
Heat recirculation
Complete burnout of NH3
Reduced emissions
Improve the combustion characteristics1,2
Vignat et al., https://doi.org/10.1016/j.proci.2022.07.054
Kin et al., https://doi.org/10.1080/00102202.2025.2464805
N
H
H
H
H2
N2

## Slide 6: Porous media combustion
Direct Pore-Level Simulation (DPLS)
and
Volume-Averaged Simulations (VAS)
NH3+air
NH3+air
VAS
DPLS
Simulation time: 2,400 CPU-h with 96 CPUs
Simulation time: 360,000 CPU-h with 3,024 CPUs

## Slide 7: Numerical modelling of ammonia combustion
Direct Pore-Level Simulation (DPLS) with solver EBIdnsFoam1
Continuity equation
Momentum conservation equation
Energy conservation equation
Species conservation equation
Ideal gas law
25 mm
25 mm
20 mm
8 mm
NH3+air
m
Outlet
Cell size
from VAS
Zirwes et al., https://doi.org/10.1007/s10494-023-00449-8

## Slide 8: Numerical modelling of ammonia combustion
Dispersion
Solid phase
Gas
phase
Energy conservation equations
1. Puri et al., Influence of dispersion length on volume-averaged simulations of ammonia/air combustion in porous media burners, Proceeding Comb. Inst. Vol 41, 2025. (Accepted)
Volume-averaged Simulation (VAS) with solver EBIvasFoam1
d, d
Ideal gas law
Darcy-Forchheimer
Pressure loss

## Slide 9: Numerical modelling of ammonia combustion
1. Puri et al., Influence of dispersion length on volume-averaged simulations of ammonia/air combustion in porous media burners, Proceeding Comb. Inst. Vol 41, 2025. (Accepted)
Volume-averaged Simulation (VAS) with solver EBIvasFoam1
d, d
Ideal gas law
Darcy-Forchheimer
Pressure loss
Material properties can be varied along the burner axis to simulate multi-layer porous burners
Dispersion
Solid phase
Gas
phase
Energy conservation equations

## Slide 10: Numerical modelling of ammonia combustion
Mean pore diameter,
Specific surface area,
Porosity,
μ-CT
Scans
Tortuosity factor,
Axial thermal conductivity factor,
Extinction coefficient,
PUMA
Effective material properties
Wm-2K-4
K
Property (unit) | SiSiC
(%) | 72.9
(mm) | 2.85
(m-1) | 891
(-) | 1.48
(Wm-1K-1) | 10.4
(-) | -0.53
(m-1) | 650
Property (unit) | SiSiC
 | 72.9
 | 2.85
 | 891
 | 1.48
 | 10.4
 | -0.53
 | 650
Volume-averaged Simulation (VAS) with solver EBIvasFoam1
1
2
3
Bedoya et al., https://doi.org/10.1016/j.combustflame.2015.07.012
Brenner et al., https://doi.org/10.1016/S0010-2180(00)00163-2
Liu et al., https://doi.org/10.1016/0272-8842(95)00125-5
25 mm
25 mm
NH3+air
implemented as temperature boundary condition in DPLS
SiSiC 15 PPI
PUMA: Ferguson et al., https://doi.org/10.1016/j.softx.2021.100775

## Slide 11: Flame structure
 | (K) | (kgm-2s-1) | (K) | (K)
 | 300 | 2.6 | 1432 | 1804
 | 300 | 2.37 | 1451 | 1819
 | 300 | 2.19 | 1418 | 1769
 | 300 | 2.6 | 1432 | 1804
 | 300 | 2.37 | 1451 | 1819
 | 300 | 2.19 | 1418 | 1769
Simulations are performed with the Stagni1 kinetic mechanism
Stagni et al., doi:10.1039/c9re00429g
from VAS

## Slide 12: Flame structure
3D Flame structure for shown by iso-surfaces of the progress variable
Individual laminar flames over channel outlets
Solid matrix acts as flame anchor

## Slide 13: Flame structure
8 mm
8 mm
mm
mm
mm
3D Flame structure for shown by iso-surfaces of the progress variable
Individual laminar flames over channel outlets
Solid matrix acts as flame anchor
Maximum penetration of unburnt fuel: 4.5 mm
mm

## Slide 14: Ammonia dehydrogenation
Distinct H2 combustion observed for higher values of the progress variable
mm

## Slide 15: Results
Minimal variation in the temperature profiles for and
DPLS flame stabilises near inlet due to high foam surface temperatures
Second temperature peak in DPLS from fixed PIM temperature boundary condition
Uniform geometric properties and unresolved flame-solid interactions in VAS lead to discrepancies with DPLS
Volume-averaging of the DPLS data and the representative elementary volume (REV) based on the cell size in VAS
REV

## Slide 16: Conclusions
Porous media combustion can improve the combustion characteristics of ammonia.
VAS performed to define PIM surface temperature boundary condition for DPLS.
Foam geometry, local flow acceleration, and temperature influence the flame structure.
Flame ignition and stabilisation affected strongly by the fixed PIM temperature boundary condition.
Hydrogen generated in the main reaction zone at intermediate progress variable values burns at high
Homogenous material and geometric material properties in VAS lead to discrepancies with DPLS.
Acknowledgements
Daniel Kretzler
Björn Stelzner
Dimosthenis Trimis
ebi-vbt
Benjamin Bock-Seefeld
Nora Brachhold
Christos G. Aneziris
The VAS and DPLS approaches will be extended to different porous geometries and operating conditions for improved NH3/air combustion.
The DPLS approach will be extended to improve the description of the gas-solid heat exchange (conjugate heat transfer, radiation).
Outlook

## Slide 17
Thank you for your attention.

## Slide 18: Flame structure
 | (K) | (kgm-2s-1) | (K) | (K)
 | 300 | 2.6 | 1432 | 1804
 | 300 | 2.37 | 1451 | 1819
 | 300 | 2.19 | 1418 | 1769
 | 300 | 2.6 | 1432 | 1804
 | 300 | 2.37 | 1451 | 1819
 | 300 | 2.19 | 1418 | 1769
Simulations are performed with the Stagni1 kinetic mechanism
Stagni et al., doi:10.1039/c9re00429g
from VAS